## Slide 1
Ethernet &
Switch Self-Learning
EC441 — Introduction to Computer Networking
Mathis Souef-Myers | Professor Carruthers | Spring 2026

## Slide 2
Ethernet Frame Format
IEEE 802.3 — What's inside every Ethernet frame?
Preamble
7 B
SFD
1 B
Dst MAC
6 B
Src MAC
6 B
Type
2 B
Payload
46-1500 B
FCS
4 B
MAC Addresses
48-bit, written in hex
e.g. A4:C3:F0:85:AC:2D
OUI = first 3 bytes (manufacturer)
Broadcast Address
FF:FF:FF:FF:FF:FF
All hosts on the LAN receive it
Used by ARP requests
Min/Max Frame Size
Min: 64 bytes (CSMA/CD)
Max: 1518 bytes
Excludes preamble & SFD
FCS (CRC-32)
Covers Dst, Src, Type, Payload
Does NOT cover preamble/SFD
Error detected → frame dropped

## Slide 3
ARP: Address Resolution Protocol
How does a host find the MAC address for a given IP?
1. ARP Request (Broadcast)
Dst MAC: FF:FF:FF:FF:FF:FF
Src MAC: AA:AA:AA:AA:AA:AA
"Who has 10.0.0.2?"
Sent to ALL hosts on the LAN
2. ARP Reply (Unicast)
Dst MAC: AA:AA:AA:AA:AA:AA
Src MAC: BB:BB:BB:BB:BB:BB
"10.0.0.2 is at BB:BB:..."
Unicast back to requester only
Key Points
ARP cache: ~20 min TTL • ARP only works within a subnet • Cross-subnet: use default gateway's MAC as Ethernet dst (IP dst unchanged)

## Slide 4
Cross-Subnet: MAC vs. IP
What changes hop-by-hop, and what stays the same?
Scenario: Host A (10.0.0.1) sends an IP packet to Host C (192.168.5.1) on a different subnet, via Router R.
Hop 1: A → Router R
Eth Src: A's MAC
Eth Dst: Router's MAC
IP Src: 10.0.0.1
IP Dst: 192.168.5.1
A ARPs for the router (gateway), not C
Hop 2: Router R → C
Eth Src: Router's MAC (new!)
Eth Dst: C's MAC
IP Src: 10.0.0.1 (unchanged)
IP Dst: 192.168.5.1 (unchanged)
Router rewrites MAC header each hop
Takeaway: IP addresses are end-to-end (never change). MAC addresses are hop-by-hop (rewritten at every router).

## Slide 5
Switch Self-Learning
Two simple rules govern every switch decision
Rule 1: LEARN from source
On every incoming frame, record the
source MAC → ingress port.
Builds the forwarding table
automatically over time.
Rule 2: FORWARD by destination
Known destination → send to
that port only.
Unknown destination → flood out
all ports except ingress.
Example Trace
1
A → B
Learn: A → port 1
Forward: Flood (B unknown)
Table: {A→1}
2
B → A
Learn: B → port 2
Forward: Port 1 (A known)
Table: {A→1, B→2}
3
A → C
Learn: Refresh A→1
Forward: Flood (C unknown)
Table: {A→1, B→2}

## Slide 6
Why 64 Bytes Minimum?
CSMA/CD requires a minimum frame size to detect collisions
The Problem
If a frame is too short, the sender
finishes transmitting before the
collision signal travels back.
The sender wouldn't know a collision
happened — data is silently lost.
The Formula
Lmin = 2τ × R
τ = d/v (one-way prop delay)
2τ = round-trip time
R = link rate
10 Mb/s, 2500 m:
τ = 12.5 μs → 2τ = 25 μs
Lmin = 25μs × 10Mb/s = 250 bits
Why 64 bytes, not 32?
The formula gives 250 bits (≈32 bytes), but IEEE 802.3 specifies 512 bits (64 bytes). The extra margin accounts for repeater delays, transceiver cable lengths, and a safety buffer. Modern full-duplex Ethernet doesn't need CSMA/CD, but the 64-byte minimum persists in the standard.

## Slide 7
Ethernet Speeds & Broadcast Storms
Speed Evolution
10 Mb/s
Manchester
1983
100 Mb/s
4B5B + MLT-3
1995
1 Gb/s
4D-PAM5
1999
10-400 Gb/s
Advanced PAM
2000s+
The Loop Problem
Broadcast Storm
A loop causes broadcast frames to
circulate forever. Each switch forwards
copies endlessly, consuming 100%
bandwidth and crashing the network.
Spanning Tree Protocol (STP)
IEEE 802.1D. Switches elect a root
bridge and block redundant links,
creating a loop-free tree. Blocked
ports reactivate if a link fails.

## Slide 8
Quick Reference
CSMA/CD (Classic Ethernet)
1. Sense channel; transmit if idle
2. Collision → jam (48 bits), abort
3. Binary exponential backoff:
r ∈ [0, 2^min(k,10) − 1]
Min frame = 2τR = 64 bytes
Modern: full-duplex switched
CSMA/CD not used in practice
Key Numbers & Facts
MAC address: 48-bit (6 bytes)
OUI: first 3 bytes (manufacturer)
EtherType 0x0800: IPv4
EtherType 0x0806: ARP
Preamble: 7B of 10101010... (PLL sync)
SFD: 10101011 (start of frame)
ARP cache TTL: ~20 minutes
Max collisions: 16, then frame dropped
The Two Switch Rules — All You Need
1. LEARN from the source MAC (record source → ingress port)
2. FORWARD by destination: known → that port | unknown → flood all other ports